## Slide 1: COE 381
16-bit Microprocessor Simulation Presentation
Class: BSc. Computer Engineering 3
Group Name: Tensor
Date: May, 2022

## Slide 2: 8252919 8259719 8266119 8263419 8264819 8253719 TENSOR GROUP MEMBERS
Alhassan Machele Ahmed
Idrisu Issaka Gibril
Tetteh Kwame Jesse
Nana Kwame Ofori-Boakye
Osei Kwaku Nana Kevin
Angmortey Benjamin Kubi

## Slide 3: INTRODUCTION 01 ISA 02 TABLE OF CONTENTS COMPONENTS 03 LIMITATIONS 04
Specifications
Overview
Instructions & Opcodes
Instruction Formats
Program Counter,
Register File, ALU,
Control Unit
Bottlenecks and
Constraints

## Slide 4: OVERVIEW 01

## Slide 5: SPECIFICATIONS
ADDRESS BIT WIDTH | 16 BITS
DATA BUS WIDTH | 16 BITS
INSTRUCTION LENGTH | 16 BITS
REGISTER COUNT | 16
INSTRUCTION COUNT | 14
TENSOR
16-BIT

## Slide 6: OVERVIEW
16-bit microprocessor
Based on RISC architecture inspired by MIPS I
Harvard Architecture – separate instruction and data memory
Memory is word-addressable (16 bits per location)
Total Memory addressable = 216 x 2 bytes = 128 KB.

## Slide 7: ISA 02
Instruction Set Architecture

## Slide 8: ISA - Overview
The microprocessor can operate on 14 basic instructions.
Each instruction falls under one of three categories
Category | Instructions
Arithmetic/Logic | ADD, ADDI, INCR, SUB, SUBI, DECR, AND, OR, XOR, NOT
Data Transfer | LOAD, STORE, MOV
Branch | JUMP

## Slide 9: ISA – Instruction Format
For simplicity, all instructions have a maximum length of 16 bits
Each of the 14 instructions follows one of four instruction formats
The instruction formats are as follows:
  R-format
  I-format
  M-format
  J-format

## Slide 10: ISA – R-Format Instructions
For instructions that utilize 3 registers.
    Rd – destination register
    Rs & Rt – source registers
Instructions: ADD, SUB, AND, OR, XOR, NOT, MOV
Some instructions won't use all three registers. Eg. NOT
​OPCODE | ​Rd | Rs | Rt
​4 bits | 4 bits | 4 bits | 4 bits

## Slide 11: ISA – I-Format Instructions
For instructions that utilize 2 registers and an immediate value from the instruction.
    Rd – destination register
    Rs – source registers
    Immediate – 4-bit immediate value
Instructions: ADDI, SUBI, INCR, DECR
​OPCODE | ​Rd | Rs | Immediate
​4 bits | 4 bits | 4 bits | 4 bits

## Slide 12: ISA – M-Format Instructions
For that utilize one register and an immediate value .
    Rd – destination/source register
    Immediate – 8-bit immediate value for memory addressing
Instructions: LOAD, STORE
For the STORE instruction, Rd is used as a source register.
​OPCODE | ​Rd | Immediate
​4 bits | 4 bits | 8 bits

## Slide 13: ISA – J-Format Instructions
For the JUMP instruction that utilizes only an immediate value .
    Immediate – 12-bit immediate value for memory addressing
Instructions: JUMP
​OPCODE | Immediate
​4 bits | 8 bits

## Slide 14: COMPONENTS 03

## Slide 15: Program Counter
The program counter loads the address of the next instruction to be executed when it is triggered by the clock.
It can also be made to branch / jump to a specified address in the instruction memory

## Slide 16: Register File
The register file is simply a housing for all 16 general-purpose registers used by the microprocessor.
Statistics:
2 read-data ports, 2 read-address ports
1 Write-data port, 1 Write-address port
1 Write-enable, 1 clock

## Slide 17: Arithmetic Logic Unit (ALU)
The ALU contains sub-circuits which are responsible for performing all arithmetic and logic operations defined in the ISA.
It uses the `ALU_SEL` control signal to determine which sub-circuit is required to perform a certain operation.
It also has carry, overflow, and zero flags.

## Slide 18: Control Unit
The control unit is the operations manager.
It emits specific control signals for each operation, that direct the other components to successfully execute the instruction.

## Slide 19: LIMITATIONS 04
What constraints does this design come with?

## Slide 20: LIMITATIONS
The I-format instructions reserve only 4 bits for the immediate, hence they can access a small range of numbers (0 to 24-1 for unsigned and –23 to 23-1 for signed)
The JUMP instruction can only go as far as memory address 212 whereas the farthest addressable memory location is 216 - 1.

## Slide 21: LIMITATIONS
The LOAD and STORE instructions can only access as far as memory address 28-1 because their instruction format (M-format) permits only an 8-bit immediate for specifying memory addresses.

## Slide 22: THANKS!